## Slide 1: Comparative geomorphology of coral reefs from a joint analysis of ICESat-2 bathymetry and multi-spectral imagery using machine learning
Karan Sunil, Adrian Borsa
University of California San Diego
Notes: UCSD Undergrad
NASA ICESAT-2
European Space Agency Sentinel-2

## Slide 2: Introduction to coral reefs
Covers 1% of the Earth’s surface.
Supports the most species per unit area for marine ecosystems.
Take between 100,000 to 30,000,000 years to fully form.
Generates $375 billion each year through tourism.
Numerous drugs developed from coral reef animals and plants.

## Slide 3: Threats to coral reefs
Healthy coral
Bleached coral
Weather related damages – cyclones, hurricanes.
Long periods of exceptionally low tides.
Increased sea surface temperatures.
Pollution – increases nutrient level that leads to higher algae growth.
Overfishing.
Notes: Bleaching – happens in shallow waters

## Slide 4: Coral reef mapping
Currently there are two global coral reef mapping projects: the Allen Coral Atlas, and the Khaled bin Sultan Living Oceans Foundation.
They map depths using satellite imagery that is validated by sonar/lidar. This process is expensive and time-consuming.
Notes: Allen Coral Atlas
Living Oceans Foundation

## Slide 5: NASA’s ICESat-2 Mission
ICESat-2 is a satellite laser altimeter making repeated observations of ice/land/ocean elevations globally.
ICESat-2’s blue-green laser penetrates water and measures shallow water bathymetry to decimeter accuracy.
Our goal – use ICESat-2 data as “ground truth” for estimation of coral reef bathymetry.
ICESat-2 projects six laser beams, separated by 90 m to 3 km.
Each beam can provide independent ground truth over a reef.
Notes: Mission (measure heights of ice sheets and sea ice)
Our goal
How calculated
Laser
Orbits

## Slide 6: NASA’s ICESat-2 Mission
ICESat-2 projects six laser beams, separated by 90 m to 3 km.
Each beam can provide independent ground truth over a reef.
ICESat-2 is a satellite laser altimeter making repeated observations of ice/land/ocean elevations globally.
ICESat-2’s blue-green laser penetrates water and measures shallow water bathymetry to decimeter accuracy.
Our goal – use ICESat-2 data as “ground truth” for estimation of coral reef bathymetry.
ICESat-2 orbits Earth 15 times daily…
Notes: Mission (measure heights of ice sheets and sea ice)
Our goal
How calculated
Laser
Orbits

## Slide 7: NASA’s ICESat-2 Mission
ICESat-2 projects six laser beams, separated by 90 m to 3 km.
Each beam can provide independent ground truth over a reef.
ICESat-2 is a satellite laser altimeter making repeated observations of ice/land/ocean elevations globally.
ICESat-2’s blue-green laser penetrates water and measures shallow water bathymetry to decimeter accuracy.
Our goal – use ICESat-2 data as “ground truth” for estimation of coral reef bathymetry.
ICESat-2 orbits Earth 15 times daily… covering 1387 different ground tracks over
3 months before starting over.
Notes: Mission (measure heights of ice sheets and sea ice)
Our goal
How calculated
Laser
Orbits

## Slide 8
India
Maldives
Track 508
ICESat-2 bathymetry profile example (Dhiffushi, Maldives)

## Slide 9: ICESat-2 bathymetry profile example (Dhiffushi, Maldives)
Track 508, Beam gt1l, 2018-10-31
photons classified as ocean surface
photons classified as reef
Classify individual ICESat-2 photons as reef or ocean
1 km

## Slide 10: Methodology
Area of rolling window = 55m2
Iterate from left to right through reef using rolling window.
Track 508, Beam gt1l, 2018-10-31
Notes: Iterate through the grid

## Slide 11
Use Interquartile range and median to generate
one representative point for each window.
Filtered results to include just back to back predictions
Track 508, Beam gt1l, 2018-10-31

## Slide 12: ICESat-2 bathymetry profile example (Dhiffushi, Maldives)
Track 508, Beam gt1l, 2018-10-31
Profile generation: Bathymetry profile created by interpolation, correcting for refraction and referencing to mean sea level using independent tide estimates.
Output is a profile of bathymetry estimates at uniform interval, with reduced noise, but also with errors

## Slide 13
Fiji
Oni-i-Lau
Moce
Track 1113
Bathymetry estimation for two atolls in Fiji, both located on ICESat-2 track 1113

## Slide 14
Fiji
Oni-i-Lau
Moce
Track 1113
Moce

## Slide 15: Sentinel-2 Multispectral Imagery (Moce, Fiji)
Band 2 – Blue (0.490 mm)
Band 8 – Near Infrared (0.842 mm)
Band 3 – Green (0.560 mm)
10-meter resolution
Global coverage
Freely/publicly available
High reflectance from clouds/land, no water penetration.
Penetrates water, moderate attenuation with depth.
Penetrates water, low attenuation with depth.

## Slide 16: Bathymetry from imagery
Blue and green light that reflects from the seafloor is attenuated to different degrees by passage through seawater.
Can use the linear relationship between [Log(blue light) – Log(green light)] to estimate depth from Sentinel-2 green and blue pixel values.
Poor performance of imagery-only bathymetry estimates necessitates using independent bathymetry data to calibrate this relationship.
Figure at right shows actual data over Moce using depths from an ICESat-2 profile and collocated Sentinel-2 pixels.
2m buffer for sea level prediction

## Slide 17: Moce, Fiji
L = Land
L
L

## Slide 18: Moce, Fiji
L = Land
L
L
Bathymetry estimates from Allen Coral Atlas do not capture shallow/deep variations inside the atoll.

## Slide 19
Fiji
Oni-i-Lau
Moce
Track 1113
Oni-i-Lau

## Slide 20: Ono-i-Lau, Fiji
L = Land
C = Clouds
L
L
L
L
C
Comparison of imagery with bathymetry estimate (right) indicates that the bathymetry is biased high, so that shallow reef is assigned positive elevations. Averaging multiple estimates reduces errors such as these.

## Slide 21: Bathymetry histograms of two Fiji reefs
Peak 1
Peak 2
Peak 3
Oni-i-Lau exhibits three peaks in its bathymetry distribution (labelled in yellow as Peaks 1-3), all separated by ~5 m.
Moce exhibits only two peaks, but these are also separated by ~5 m and may align with Oni-i-Lau peaks after estimates are averaged.

## Slide 22: Conclusions
We can estimate coral reef bathymetry anywhere on Earth using a combination of satellite imagery and satellite bathymetry.
ICESat-2 photon data provide shallow bathymetry at 1-meter horizonal resolution, while satellite Imagery is at a 10m resolution suggesting that we can use higher-resolution imagery for bathymetric estimates
Applications:
  From reef depth distributions, we can identify which corals are at a higher risk of endangerment due to sea surface warming.
  We can study the effect of natural disasters such as hurricanes by analyzing before and after bathymetry.